## Slide 1: Mobile Self-Balancing Robot
Team SEGWAY
William Bednar, Brian Gonzalez, Ye Xin, Adam Stein, and Zachary Lowe

## Slide 2: Outline
Introduction and Background
Prototype
Demo
Control Software
Tuning
Communication
Manual Control
Challenges
Potential Improvements

## Slide 3: Project Description
Built a self-balancing robot as an exercise in control systems engineering as well as hardware/software integration

## Slide 4: Goals
Stable, upright robot
Fast movement
Travel over various terrains and inclines
Position awareness
Functional application such as serving food and drinks
Line following

## Slide 5: Last Semester
Collected resources
Learned about similar projects online
Prototype

## Slide 6: Video: old prototype in action
https://www.youtube.com/watch?v=1i9Vt7IHzNo

## Slide 7: Scaling Up

## Slide 8: Current Version
Important Features
  Large wheels with treads
  Lightweight frame
    Metal brackets
    Foam board
  Better motor shield
  Head, hat, and sunglasses

## Slide 9: Remote
Wired
Kill switch
Knob
  Manual “PID”
  Parameter adjustment
  Steering
  No longer used
Button
  Previously coast
  Hold to transmit telemetry data

## Slide 10: Hardware Layout

## Slide 11: Cost
Frame - $60
Wheels & motors - $160
Motor controller - $50
Existing parts - $95
  Arduino
  Sensor and Bluetooth modules
  LiPo battery
Total $365

## Slide 12: Demo
A brief live demo
Videos from outside
  https://www.youtube.com/watch?v=a9SOppzgmxc

## Slide 13: Control Concepts
cs.brown.edu
Complementary filter
Negative feedback - error calculation
ChrisMarion.net

## Slide 14: Control Software
thetaDotG = -gyro.g.y / gyro_scale;
thetaA = asin(-accel.getZ() / 9.81) - accelOffset;
// Calculate new theta/error estimates
float dThetaG = thetaDotG * dt; // integrate gyro reading
estTheta = highpassCoeff * (estTheta + dThetaG); // high-pass gyro
estTheta += lowpassCoeff * thetaA; // low-pass accelerometer
estError = estTheta - targetAngle;
// Compute & limit the error integral
errorInt += estError * dt;
// Calculate PID output
output = Kp*estError + Kd*thetaDotG + Ki*errorInt;
KerryWong.com

## Slide 15: PID Controller – Tuning
We manually tuned the PID controller by setting Ki and Kd to zero and adjusting Kp until the system oscillated.
Kp was set to half that value, and Ki was then increased until the oscillations were reasonably small.
Kd was then increased until the system responded fast enough.

## Slide 16: PID Controller – Tuning
Effects of increasing parameters independently:
Parameter | Rise time | Overshoot | Settling time | Steady-state error | Stability
Kp | Decrease | Increase | Small change | Decrease | Degrade
Ki | Decrease | Increase | Increase | Eliminate | Degrade
Kd | Minor change | Decrease | Decrease | No effect in theory | Improve if Kd small

## Slide 17: Tuning Program
Made tuning much easier
Also displays data sent from the Segway
Written in C# utilizing the .NET Framework
Probably Windows only
  Might run under Mono

## Slide 21: Communication
Bluetooth serial module
Transparent serial cable replacement
Binary protocol for efficiency
  1 byte message code followed by data
  Data length varies by message code
8-bit CRC
Unambiguous framing
No acknowledgements or retransmission

## Slide 22: Mouse Control
GUI for mouse control
Click to move the dot
Vertical axis is angle (acceleration)
Horizontal axis is steering

## Slide 23: A better controller?

## Slide 24: Challenges
Sensor limitations
  Vibrations in frame cause jitter in sensor readings
  Target angle is affected if the sensor comes loose or shifts position
  Hard to mount – unusable screw holes and no flat side due to through hole connector
Motor limitations
  Identical voltages produce different speeds on each motor

## Slide 25: Potential Improvements
Speed limiting
  Lean back to reduce speed before falling over
Maintain position
  Wheel encoders – need more pins
  Second PID controller to control the target angle
Improved remote control protocol
Functional tasks such as serving food and drinks
Autonomous movement
Phone app

## Slide 26: Conclusion
Robot was ultimately able to balance and recover from most disturbances.
Maintains its position relatively well when undisturbed.
User control interfaces allowed some direct control of robot movement.
We did not end up having time to implement autonomous movement heuristics like line following.

## Slide 27: Questions?
https://www.youtube.com/watch?v=-faroIVwW9g